## Slide 1: Getting Data in the Lab
ME5990
Spring 2016
Jason D. Sommerville
Copyright © 2016 UPVI, LLC. Redistribution is prohibited.

## Slide 2
2
Phenomenon
Cooling of Tea
Transducer
Thermocouple
Signal Conditioner
Amplifier, Low pass filter
DAQ Hardware
NI CompactDAQ
Computer
Brought to you by IT
Analysis
Curve fitting
Plotting
DAQ
Analog Input
Storing Data
HDF5 Files
Thesis/
Dissertation
Graduate!
Software Basics

## Slide 3: Software Development from 30,000 ft
Why do we develop software?
  To interface with the real world via hardware
  For flexibility
  For extensibility
  To enable us to acquire and process more than we could by hand
What do we need?
  A problem
  A plan (1)
  A computer
  A language (3)
  Other tools
    Editor or integrated development environment
    Documentation tools (e.g. word processor)
    Source code control (2)
    Issue tracking database
Notes: Whiteboard why
Whiteboard what we need

## Slide 4: Source Code Control (SCC)
Also called Revision Control System (RCS) or Version Control system (VCS)
Keeps track of edits to code
  Allows for review of history
  Allows for global, long-term undo
Allows multiple people to work on code simultaneously
  With minimal conflicts!
Allows for branching and merging
Notes: Whiteboard branching and merging

## Slide 5: NI 401 Past
https://web.archive.org/web/20130405041937/http://www.ni.com/news/releases/april9801.htm
https://web.archive.org/web/20130405041937/http://www.ni.com/news/releases/april901.htm
Notes: Whiteboard branching and merging

## Slide 6: Laboratory Software Choices
Language | Ease of Language | Development Environment | Data Acquisition | Instrument Control | Analysis Capabilities | Debugging Capabilities | UI Development Ease | UI Development Capabilities | Initial Cost
C/C++ | 1 | 5 | 3 | 4 | 2 | 5 | 1 | 5 | Low
Matlab | 3 | 4 | 2 | 3 | 5 | 3 | 3 | 2 | Med
Python | 4 | 2 | 2 | 4 | 4 | 4 | 4 | 4 | Free
LabVIEW | 5 | 4 | 5 | 5 | 4 | 4 | 5 | 3 | Med
My opinion on the effectiveness of the languages for laboratory usage. Scale of 1 = worst to 5 = best.
Notes: With what languages is the class familiar?

## Slide 7: What is LabVIEW?
Programming language
  Graphical
  General purpose (but…)
  Data flow
Great for
  Data acquisition
  Data storage
  Instrumentation control
  Simple to moderately complex UIs
  Rapid prototyping of complex software
  Programming real time systems and FPGAs*
Okay for
  Data analysis and plotting
Not so good for
  Complex UIs
  Embedded systems not supported by NI
*Provided you are programming an NI or compatible RT or FPGA system

## Slide 8: LabVIEW Environment
Front Panel
User interface goes here
Block Diagram
Code goes here
Control Palette
(FP Only)
Function Palette
(BD Only)
Tools Palette
Notes: Palettes turn on and off from view menu
Also, right click and ctrl+right click

## Slide 9: Coding Elements
Data types
Flow control
  Loops
    Shift registers
    Auto-indexing/building
  Parallel loops
  Case statements
  Event structure
Error Handling

## Slide 10: Design Patterns
Using SubVIs
State Machine
Master-Slave
Producer-Consumer
Message Handler

## Slide 11: Analysis
LabVIEW has numerous functions for analyzing data
  May not be the best choice for all analysis
  Is your analysis simple, consisting of only a few steps?
  Does your analysis need to be online during your acquisition?
  Do you know exactly what you want to do to analyze your data?
Other choices:
  Diadem
  Igor
  Matlab
  SciPy + NumPy + Python
  It is possible to incorporate analysis functions from Diadem or Matlab into LabVIEW
Some of the palettes with analysis functions
Notes: ChartsAndGraphs.vi

## Slide 12: Saving Data
What to save?
  Dataset: The raw data (if feasible)
  Intermediate results (standard deviations and other simple processing)
  Attributes (aka properties, metadata):
    Date
    Time
    Purpose of data (comments)
    Acquisition information (instrumentation, settings)
  You can’t save too many details!
    You never know what you’ll wish you had recorded latter
Saving processed results?
  Best to save in separate files
  Use attributes to describe the raw data source and processing methods
Notes: ChartsAndGraphs.vi

## Slide 13: Saving Data: What Format?
File I/O
  Text, CSV
  Raw binary
  Self-describing formats
    TDMS
    NetCDF
    HDF5
    Etc.
Databases
  Use Simple Query Language (SQL) to write, search, etc.
  Data organized in cross-linked tables
  MySQL, postgresql, SQLite, Access, Oracle, etc.
TDMS
Raw
Binary
ASCII Text
Notes: ChartsAndGraphs.vi

## Slide 14: Types of DAQ: Signal Acquisition
Convert analog voltage signals into digital data
Single-shot or timed measurements
Analog Input
Digital Input
Counter/Timers
Use an analog-to-digital converter
Examples: temperature, sounds, voltage
Single-shot or timed
Single bit or bus
Example: proximity sensor, photointerrupter
Count events
Time events
Examples: encoders, pulse train timing, delay timing, delay generation
101110110100 101110100101 011001100101
110011000101 011100101010 110110001000
1 or 0
Buffer
555
4, 5, 6, …
10 ms
10 ms
Counter/Timer

## Slide 15: Types of DAQ: Generation
Convert digital data into analog waveforms
Single-shot or timed generation
Analog Output
Digital Output
Counter/Timers
Use a digital-to-analog converter
Examples: sound, system excitation, motor control
Single-shot or timed
Single bit or bus
Generating a slow trigger, controlling an LED, controlling a bus
Control timing
Examples: Pulse train generation, delay generation
1 or 0
Buffer
555
4, 5, 6, …
10 ms
10 ms
Counter/Timer
101110110100 101110100101 011001100101
110011000101 011100101010 110110001000

## Slide 16: How to chose a transducer
What type of measurement do you need to make?
Calibration Curve
  Range
    Input range (25 – 300 ºC, 1 – 100 mN, etc.)
    Output range (0 to 10V, -5 to 5 V, 4 to 20 mA, etc.)
  Sensitivity—How well can change be detected?
How good is the measurement?
  Accuracy (±1 ºC, ±0.1 mN, etc.)
  Precision (repeatability)
  Linearity—can be handled in software
  Drift—Change in calibration over time
  Hysteresis—is it the same going up as coming back down?
Timing
  Response time
  Bandwidth (1 Hz, 100 kHz – 1 MHz, etc.)
Other considerations
  Analog or digital
    Analog: voltage, current, impedance, etc.
  What signal conditioning or excitation/power does it require?
  How will I connect it to my DAQ system?
  Environmental isolation
    Voltage, temperature, noise, vacuum, water, etc.
  Ruggedness
  Cost
A: All this info should be on the transducer’s datasheet or specification sheet
Q: Where do I find this stuff?
(which should be available from the manufacturer’s website)

## Slide 17: How to choose DAQ hardware
What type of signals do you need to acquire/generate?
How many channels of each type?
After external conditioning, what will the polarity and range of your signal be?
DI/SE?
What resolution do you need across that range?
What bandwidth do you need?
At what rate do you need to acquire/generate the data?
  Note that bandwidth ≠ sampling frequency, but related
  How precise are you timing requirements? Can you use software timing?
  How much time-skew is acceptable?
Memory depth if signals cannot be transferred to system memory
Connectors
Form factor
Computer interface (e.g. PCIe, PXI, USB, etc.)
Software interface
Front panel controls
Cost

## Slide 18: The Mantra
Create
Configure
Start
Read/Write
Stop
Clear

## Slide 19: Continuous Sampling
Acquiring data forever
But how will I graduate?
Specify number of samples to read.
Defaults to “all available.”
See also NI Example: Voltage – Continuous Input.vi
Notes: Modify Finite into Continuous

## Slide 20: Other DAQ Topics Covered
Analog Output, DIO, Counter-Timers
Triggering
External Clocking to synchronize acquisition between devices
Integrating DAQ with design patterns

## Slide 21: Instrument Control
There are several communication links: GPIB, USB, Serial, etc.
Serial is the most common, but also the biggest hassle.
Make sure to configure your instruments for the communication link
Find an instrument driver
If you can’t, or you need to modify the driver you find:
  Many instruments use text, “message-based” protocols such as SCPI
  Get the protocol documentation
  Use string functions to format and parse messages
Communication
Interface
Measurement,
etc.

## Slide 22: Much more to explore
Real-time DAQ and LabVIEW RT
LabVIEW FPGA, esp. with compactRIO
Designing and implementing control systems (MEEM 5750)
Calling external code libraries
LabVIEW code optimization
LabVIEW’s threading and priority system
Signal conditioning design: filters, isolation, etc.
Signal processing, data analysis, etc. (MEEM 5700)
Image acquisition and processing
Motion control
Network communications
Remote systems
Inter-VI communciation
Dynamic VI calls
DAQ/Instrument Control from other languages
  Python
  C/C++
  Matlab
  Etc
Embedded measurement systems
Tracking down noise problems
Designing experiments to be statistically valid (MEEM 5670)

## Slide 23: Thanks for being my guinea pigs!
I hope you found the experiment successful