## Slide 1: Getting Data in the Lab
ME5990
Spring 2016
Jason D. Sommerville
Copyright © 2016 UPVI, LLC. Redistribution is prohibited.

## Slide 2: Tidbits I Missed
LabVIEW License
Control and indicator default values
Cluster order
Post questions in the discussion section of Canvas
Notes: These are up front so that they get properly incorporated for next time.

## Slide 3
3
Phenomenon
Cooling of Tea
Transducer
Thermocouple
Signal Conditioner
Amplifier, Low pass filter
DAQ Hardware
NI CompactDAQ
Computer
Brought to you by IT
Analysis
Curve fitting
Plotting
DAQ
Analog Input
Storing Data
HDF5 Files
Thesis/
Dissertation
Graduate!
Software Basics

## Slide 4: Software Development from 30,000 ft
Why do we develop software?
  To interface with the real world via hardware
  For flexibility
  For extensibility
  To enable us to acquire and process more than we could by hand
What do we need?
  A problem
  A plan (1)
  A computer
  A language (3)
  Other tools
    Editor or integrated development environment
    Documentation tools (e.g. word processor)
    Source code control (2)
    Issue tracking database
Notes: Whiteboard why
Whiteboard what we need

## Slide 5: Software Design Life Cycle
Requirements Analysis
Design
Implement
Test
Evolution

## Slide 6: Grad Student’s SDLC
Implement
Evolution
Notes: Don’t do this!

## Slide 7: Software Design Life Cycle
Requirements Analysis
Design
Implement
Test
Evolution
What must be done?
How will the user do it?
How the programmer make it happen?
Program!
Document!
Does it do what it’s supposed to?
Time passes.
Needs change.

## Slide 8: Software Design Lifecycle
When developing any software, use it!
Even if you do the requirements analysis and design on a napkin
Absolutely required for large projects or projects with multiple people working on it
(We won’t be using much of the Evolution portion in this class.)

## Slide 9: Source Code Control (SCC)
Also called Revision Control System (RCS) or Version Control system (VCS)
Keeps track of edits to code
  Allows for review of history
  Allows for global, long-term undo
Allows multiple people to work on code simultaneously
  With minimal conflicts!
Allows for branching and merging
Notes: Whiteboard branching and merging

## Slide 10: SCC Choices
Numerous open source choices
  In the stone age people simply copied files and folders and put dates on them
  CVS is the senile grand-daddy
  SVN is the aging prince
  git is the scrappy upstart
  Mercurial is also popular
  Bazaar is dead (don’t pick this one)
Commercial choices
  Perforce
  Microsoft Team Foundation Version Control
  IBM Rational ClearCase

## Slide 11: The github repos

## Slide 12: Forking the class git repository
Create a github account
E-mail me your github account username
Wait for a confirmation e-mail from github notifying you that you’ve been added to the MichiganTech organization
Goto http://github.com/MichiganTech/me5990_spring2016
Fork the repo by pressing the “Fork” button

## Slide 13: Forking the class git repository
Be sure to add me (jdsommer) as a collaborator to your fork!
  If I can’t see it, I can’t give you credit. Also remove any inheritted users

## Slide 14: Git tasks
Use the git bash shell (or your favorite GUI tool)
Getting a local copy of your github repo (the first time)
  Sets up the “origin” name used for future pulls and pushes
  git clone http://github.com/<username>/me5990_spring2016
Updating your local copy from your github repo (every other time)
  git pull origin
Adding a file
  Create the file, then
  git add <filename>
Deleting a file
  Don’t delete it without using git
  git rm <filename>
Committing your changes
  git stage then
  git commit
Pushing your changes to your github repo
  Must do this to get credit!
  git push origin

## Slide 15: Pulling Updates from the Class Repo
Be sure to pull updates regularly, especially before starting new homework assignments.
In your local repo, execute
  git remote add class https://github.com/MichiganTech/me5990_spring2016
  This need be done only once
Then, to pull the update execute
  git pull class master
This will pull any changes down from the class repository and merge them with your local repository.
  There is potential for conflicts if you have edited files that I have edited.
  Follow git’s instructions that it will print after executing git pull to resolved the conflict

## Slide 16: Good SCC Practices
How often should I check in (commit) my changes?
  Working by yourself:
    As often as you like, but no less often than when every feature or modification is completed
  Working with others:
    When a feature is completed and tested
    Follow company/project guidelines
Be sure to use commit descriptions
Label or branch “public releases” for future reference

## Slide 17: Update This Slide for git!!!
SVN
Repo
rev 1
SVN
Repo
rev 2
Pulls head revision
Alice
Bob
rev 1*
Pushes updates
Tries to push updates, fails
Alice
rev 1*
Alice
rev 1*
Alice
rev 2*
Pulls head and
resolves conflicts
SVN
Repo
rev 3
Pushes updates
* denotes a modified revision that has not been committed
Time
Bob
rev 3
Pulls head
On Server
On Bob’s PC
On Alice’s PC

## Slide 18: Laboratory Software Choices
Language | Ease of Language | Development Environment | Data Acquisition | Instrument Control | Analysis Capabilities | Debugging Capabilities | UI Development Ease | UI Development Capabilities | Initial Cost
C/C++ | 1 | 5 | 3 | 4 | 2 | 5 | 1 | 5 | Low
Matlab | 3 | 4 | 2 | 3 | 5 | 3 | 3 | 2 | Med
Python | 4 | 2 | 2 | 4 | 4 | 4 | 4 | 4 | Free
LabVIEW | 5 | 4 | 5 | 5 | 4 | 4 | 5 | 3 | Med
My opinion on the effectiveness of the languages for laboratory usage. Scale of 1 = worst to 5 = best.
Notes: With what languages is the class familiar?

## Slide 19: What is LabVIEW?
Programming language
  Graphical
  General purpose (but…)
  Data flow
Great for
  Data acquisition
  Data storage
  Instrumentation control
  Simple to moderately complex UIs
  Rapid prototyping of complex software
  Programming real time systems and FPGAs*
Okay for
  Data analysis and plotting
Not so good for
  Complex UIs
  Embedded systems not supported by NI
*Provided you are programming an NI or compatible RT or FPGA system

## Slide 20: LabVIEW Environment
Front Panel
User interface goes here
Block Diagram
Code goes here
Control Palette
(FP Only)
Function Palette
(BD Only)
Tools Palette
Notes: Palettes turn on and off from view menu
Also, right click and ctrl+right click

## Slide 21: Front Panel
Place and arrange controls, indicators and decorations
  Controls
    Inputs to the VI
  Indicators
    Outputs from the VI
Create VI Icons and Connector Panes
Control Execution

## Slide 22: Placing Controls

## Slide 23: Toolbar
Run: start the VI’s execution
Run continuously: run VI in a loop, endlessly (rarely used)
Abort: This is not stop It’s ABORT!
Run
Run Continuously
Abort
Pause
Alignment, ordering, etc.
Font

## Slide 24: Block Diagram
Control
Indicators
Comment
Node (Function)

## Slide 25: Toolbar
Execution Highlighting: watch the VI run (super slowly)
Retain Wire Values: Allows use of wire probes after VI exits
Step execution: Execute one node at a time
Step Execution
Retain Wire Values
Execution Highlighting
Automatic BD “Cleanup”

## Slide 26: Control/Indicator Terminals
Indicator Pair
Control Pair

## Slide 27: Building a Simple VI
Watch the Amazing Dr. Sommerville build a simple VI.
Notes: Build this.

## Slide 28: Dataflow
Watch VI run
Notes: Run ApmB.vi

## Slide 29: Numeric Control and Indicator Types

## Slide 30: Data Types (Incomplete)

## Slide 31: Data Types—Why should I care?
Using the proper data type forces the user/programmer to handle the data correctly
Using an unnecessarily large play will adversely affect performance
Using a numeric data type which is too small can lead to loss of precision or catastrophic rollover
Some numbers may not be exactly represented by floating values.

## Slide 32: Integer Data Types
LabVIEW Name | Bits | Minimum | Maximum | Other Common Names
I8 | 8 | -128 | 127 | char, byte
U8 | 8 | 0 | 255 | unsigned char, unsigned byte
I16 | 16 | -32768 | 32767 | short
U16 | 16 | 0 | 65535 | unsigned short, word
I32 | 32 | -2147483648 | 2147483647 | int, long
U32 | 32 | 0 | 4294967296 | unsigned int, unsigned long, dword
I64 | 64 | ~-9x1018 | 9x1018 | qword, long long
U64 | 64 | 0 | ~2x1019 | unsigned qword, unsigned long long
Unsigned:
N bits (e.g. 32)
N-1 bits (e.g. 31)
Signed:
lsb
msb
lsb
msb
sign

## Slide 33: Binary, Decimal and Hex
Understanding how integers are stored is useful for understanding the effect of your data choice on program speed and data size
Binary flags in integers are often used in instrument communication protocols
Best TV Show Ever!

## Slide 34: Floating Point Data Types
LabVIEW Name | Bits | Mantissa | Exponent | Decimal Exponent Range* | Decimal Digits of Precision (approx) | Other Common Names
SGL | 32 | 23 | 8 | -38 – 38 | 7 | float, real
DBL | 64 | 52 | 11 | -308 – 308 | 16 | double
EXT** | 80 | 64 | 15 | -4932 – 4932 | 19 | long double
* Does not include subnormal values.
**Platform dependent. Values for Windows platform shown.
lsb
msb
lsb
msb

## Slide 35: Floating Point Data Types
How to calculate minimum and maximum exponents?
How to calculate digits of precision
If e is the number of bits in the exponent, the decimal exponents range is from
-2^(2^(e-1)-1)
to
2^(2^(e-1))
If m is the number of bits in the mantissa, the approimate decimal precision is
log10(2^m)
digits.

## Slide 36: Data Types—Which One?
Do restrict the data type to the type of information expected or required
  Counting—use unsigned integers
  Real numbers—use floats
  Use strings only when necessary
Don’t unnecessarily restrict the data type
  E.g. don’t use integers to represent length

## Slide 37: Numeric Data Types--Changing
Right-click on control, indicator or constant
Representation dialog

## Slide 38: Clusters
Cluster group related, differently-typed data together
Equivalent to C/C++ struct or Fortran record
Classic example: address book entry
Scientific examples:
  Data from multiple sensors
  Meta-data (aka attributes)
Build an cluster

## Slide 39: Working with Clusters
Bundle
Bundle by name
Unbundle
Unbundle by name
Demonstrate wiring clusters

## Slide 40: Arrays
Set of identically-typed values
N-dimensional
  1-D: list, vector, etc.
  2-D: table, matrix, image, etc.
  3-D: tensor, gridded volume
  4-D+: ???
1-D and 2-D arrays very common in data acquisition
Create an array

## Slide 41: Working with Arrays
Array palette has numerous functions
Index array
Replace array subset (or element)
Build array
Array subset
And many more!
Work with arrays on screen

## Slide 42: Arrays or Clusters?
All elements of the same type
Elements express dimensionality (e.g. space, time, frequency, etc.)
Elements should be indexed
Members are of different types (including different numeric types)
Members express differing concepts, but are related
Members should be named

## Slide 43: Arrays <-> Cluster

## Slide 44: Arrays or Clusters—Why not both?
A common data type is the table
Naturally expressed as a 1-D array of clusters
LabVIEW display not limited to the above control

## Slide 45: Loops
For Loop
Iterate until stop condition
Iterate while true condition
While Loop
Iterate N times
Conditional may be added
Stop Terminal
(click to switch)
Index Number
(0-based)
N Count
Notes: RollN.vi and RollUntil.vi

## Slide 46: Auto-indexing
Arrays automatically index at input terminals
Arrays automatically built at output terminals
Indexing/non-indexing by right-clicking on terminal
Auto-building efficiency
  For loops: efficient
  While loops: inefficient
Auto-indexing input terminal
Auto-building output terminal
Runs as many iterations as array input
(unless wired)
Notes: AutoIndexing.vi

## Slide 47: Auto-indexing
Enabling/Disabling indexing on input tunnels
Enabling/Disabling indexing/concatenating on output tunnels
Notes: AutoIndexing.vi

## Slide 48: Auto-indexing
Tunnel options with scalars in the loop
Tunnel options with arrays in the loop
IndexingTypes.vi
Notes: AutoIndexing.vi

## Slide 49: Shift Registers
Use previous values in a loop
  Value at output terminal appears at input terminal on the next iteration
Create by right-clicking on loop boundary
Input terminals usually must be initialized
Shift register input terminal(s)
Shift register output terminal
Notes: ShiftRegisters.vi

## Slide 50: Parallel Loops
Parallel loops operate simultaneously
  According to dataflow
  Similar to multiple threads
Useful for
  Processes that operate at different rates
  Separating UI code (event-based) from DAQ code (time-based)
But how do I communicate from one loop to another?
  Beyond scope
  Local variables, global variables, message queues, semaphores, NI-PSP and other network-based solutions.
Notes: LV1M37_Parallelism
Demonstrate flow control issues.
Modify LV1M37 to use a local variable stop button

## Slide 51: Case Statements
Case statements allow if-then-else or switch-type decisions
CaseStatement.vi
Conditional terminal
Case selector
Notes: Show CaseStatement.vi
Modify to use multiple bools and array search
Modify to use Ring
Modify to use Enum

## Slide 52: Case Statements
All output terminals must be wired unless “Use Default if Unwired” is selected
Unwired output tunnel => Broken VI
Unwired output tunnel, + “Use Default if Unwired” => Working VI
Notes: Show CaseStatement.vi
Modify to use multiple bools and array search
Modify to use Ring
Modify to use Enum

## Slide 53: Rings
Controls and indicators which map strings to integers
  Is cosmetic only!
Useful for
  Limiting or suggesting user selections
Create on the front-panel or the block diagram
  Then populate the items by
  A) typing directly into the control/indicator/constant
  B) selecting “Edit Items…”

## Slide 54: Enumerations
Enumerations give names to numbers like Rings, but…
An enumeration is a user-created datatype
  Derived from unsigned integers
Useful for
  Limiting user selections
  Limiting programmer choices
  Making code readable
Create on the front-panel or the block diagram
  Then populate the items by
  A) typing directly into the control/indicator/constant
  B) selecting “Edit Items…”
Cast to U32 (U16 or U8) with standard conversion functions (Numeric -> Conversion palette)

## Slide 55: Classic Event-Driven VIs
ClassicEventDrivenVI.vi
Typically, event driven VIs now use the event structure, but this construction can still be useful and is definitely instructive.

## Slide 56: Sequence Statements
Force sequence of operations
No way to enforce sequencing via dataflow

## Slide 57: Sequence Statements
Stacked Sequence Structures and Sequence Locals
Sequence Local
Notes: Show CaseStatement.vi
Modify to use multiple bools and array search
Modify to use Ring
Modify to use Enum

## Slide 58: Error Handling
Error Handling is primarily done through the Error Cluster
Error Cluster has three elements:
  Boolean “status” error occurred
  I32 “code” error code
  String “source” location and message
Standard error terminals on bottom corners
Error handling dialogs

## Slide 59: Case Statements—Error Cluster
Standard error codes are enumerated in the help file.

## Slide 60: Error Handling (cont.)
USE IT!!
  Almost all the VIs and primitives that you use have error cluster outputs.
  Unexpected things go wrong, particularly for novices.
  Even if you don’t understand the error, someone else probably does
Automatic error handling
  Per VI
  Enabled by default for unwired error outputs
  Recommended error handling settings (for intermediate+ developers)

## Slide 61: Waveform Datatype
Used to represent a time series of data
  Could actually be any regularly sampled data
A special cluster
  t0: Timestamp, time of Y0
  dt: DBL time step between Y points
  Y:1-D Array of numeric type
  (attributes: variant)
Uses different bundle and unbundle
  On the waveform palette

## Slide 62: Waveform Datatype
Default input/output type for timed DAQ
  More on that later
Used by numerous signal generation and processing functions
  Generate function (sin, square, etc.) wave data
  Extract DC and RMS values
  Apply digital filters

## Slide 63: We Have Charts and Graphs
Waveform Charts
  Keep a log of the previous data written to the terminal
  If x-axis rate is constant, set Multiplier in the properties
Waveform Graphs
  Plot data vs. time or otherwise regularly spaced x-axis
  Uses, t0, dt and Y data array
  Use Build Waveform to specify t0, dt and Y data
X-Y Graphs
  Plot Y array of data vs. X array of data
  Use Build Cluster to pair arrays
All charts and graphs can support multiple traces
Notes: ChartsAndGraphs.vi

## Slide 64: We Have Charts and Graphs
Properties may be accessed by right clicking on the chart/graph.
  Plot styles and colors
  Axes styles and labels
  Gridline coloring and spacing
(Advanced!) Properties may also be modified via properties nodes
  Right-click on terminal or control and select Create->Property Node
  Allows more programmatic modification
  Note: other controls and indicators have property nodes also.
Notes: ChartsAndGraphs.vi

## Slide 65: Project Update
Several professors may have projects in need of your help
  Dr. John Beard: jebeard@mtu.edu
    Instrumenting a vehicle suspension
    Controlling an orthopedic device
  Dr. Jeff Allen: jstallen@mtu.edu
    Instrumenting a solar water heater
  Dr. Ezequiel Medici: efmedici@mtu.edu
    Field infrasound detection system
  Dr. Scott Wagner (School of Technology): swwagner@mtu.edu
    Tube forming process monitor
  Dr. Jayaraman Gopal: gjayar@mtu.edu
    Pedestrian protection system for motorcycles and scooters
Note that you must be a net positive for the professors. They’ll get you started, but you must work independently.

## Slide 66: Project Update
I have a collection of sensors available for independent projects
  Pressure
  Humidity
  Thermocouples
  Accelerometers
  Access to load cells
Stop by my office to have a look
I need them all back in the same condition you take them
You may need to find power supplies or other equipment to make them work

## Slide 67: Quiz 1: Factorial

## Slide 68: Other Announcements
No class Thursday
  Homework still due
Start bringing your DAQs
  We may use it in class next lecture
Quiz next Tuesday

## Slide 69: SubVIs!
“LabVIEW sucks because I’ve got all these wires running all over the screen and I have to scroll everywhere and I can’t see the whole thing at once. Wah!”
–Novice LabVIEW Programmer

## Slide 70
http://thedailywtf.com/articles/comments/Labview-Spaghetti

## Slide 71: SubVIs!
SubVIs are like functions
  Enable modular programming
  Enable easier testing
  Make high-level VIs make sense
But how do I make them?
  Use the Connector Pane and the Icon
  Wire controls and indicators to connector pane
  Making a SubVI from scratch
  Collecting code into a subVI
Notes: Make a subVI for adding two numbers and subtracting a third.
Call it from Master.vi
Rebuild Master and show how to collect code into a subVI
Signal Generator by Duration.vi

## Slide 72: The Connector Pane
Wire controls and indicators to the connector pane
  Select the wiring tool
  Click on the desired terminal
  Click on the control/indicator you wish to associate with it
Notes: Make a subVI for adding two numbers and subtracting a third.
Call it from Master.vi
Rebuild Master and show how to collect code into a subVI
Signal Generator by Duration.vi

## Slide 73: The Connector Pane
Changing the pattern
  You can change the connector pattern by right-clicking on the icon or connector pane
  Also may flip and rotate the pattern
Right click also gives access to disconnecting controls/indicators from terminals
Notes: Make a subVI for adding two numbers and subtracting a third.
Call it from Master.vi
Rebuild Master and show how to collect code into a subVI
Signal Generator by Duration.vi

## Slide 74: Connector Pane Style
The following style guidelines help make subVIs easier to use
Prefer the 4x2x2x4 pattern
Avoid patterns with more than 16 terminals
  I say 12
  Use clusters to reduce the number of terminals
Wire inputs on the left
Wire outputs on the right
Wire error input to bottom left
Wire error output to bottom right
From LabVIEW Development Guidelines, 2003

## Slide 75: Terminal Behavior
Terminals may be
Required: caller must wire this terminal or the VI will be broken
  Input terminals only
Recommend: caller should wire this terminal
  On inputs, default values will be used if unwired.
Optional: caller need not wire this terminal in most situations
Notes: Make a subVI for adding two numbers and subtracting a third.
Call it from Master.vi
Rebuild Master and show how to collect code into a subVI
Signal Generator by Duration.vi

## Slide 76: Editing the Icon
DO! Edit the icon of your subVIs (even it its lousy)
Right-click on icon -> “Edit icon…”
Or double-click on icon
Notes: Make a subVI for adding two numbers and subtracting a third.
Call it from Master.vi
Rebuild Master and show how to collect code into a subVI
Signal Generator by Duration.vi

## Slide 77: Using SubVIs
SubVIs may be placed in multiple ways
“Select VI…” palette menu
Drag file from file explorer
Drag from VI icon
1.
2.
3.

## Slide 78: Where LabVIEW Looks for SubVIs
LabVIEW first looks for Vis of the appropriate name already in memory.
Then it follows the search path:
  Tools -> Options menu, then
Relative to the top-level calling VI
Previous locations in which the VI was found
vi.lib folder of LabVIEW installation
user.lib folder of LabVIEW installation
instr.lib folder of LabVIEW installation
Others

## Slide 79: Debugging SubVIs
SubVIs may be stepped into, over, or out
Into: When paused at a subVI, step into the subVI and examine its execution
  Use when you are not sure if the subVI is behaving properly
Over: When paused at a subVI, step over the VI, executing it without examining it
  Use when you are sure the subVI is not the problem
Out: When debugging inside a subVI, step complete the execution of the subVI and return to the caller
Note! These same behaviors also apply to loops. Read the tool tip over when hovering over the debug buttons to confirm the action you are about to perform.

## Slide 80: Debugging SubVIs (cont.)
In this example, VI execution is stopped at a subVI with a breakpoint. The user is preparing to step into the subVI and debug its execution.

## Slide 81: SubVIs: Conclusion
SubVIs allow for cleaner code
  Code easier to read because one can quickly understand what a SubVI does by looking at it (mostly).
Functional blocks can be individually tested
Commonly used functions can be encapsulated
  If the SubVI is changed, call callers inherit the improved behavior
    Note: this usually a great thing, but occasionally it can be disastrous!
  Code can be reused in multiple programs
USE THEM (or else!)

## Slide 82: Review
LabVIEW is great for data acquisition
LabVIEW programs call Vis
  Front panel is UI
  Block diagram is code
  FP and BD linked by controls and indicators
  Code executes in dataflow
Datatypes
Decisions made with case statements
For loops and while loops to repeat code
  Arrays auto-index and auto-build
  Shift registers to use and update values in a loop
  Parallel loops execute simultaneously
Charts and Graphs
  Waveform Charts keep a history
  Waveform Graphs for plotting data with regular x intervals
  X-Y charts for irregular data
Use SubVIs to modularize code
  Controls and indicators are inputs and outputs
  Use Connector Pane to associate controls and indicators
  “Create SubVI”
Error Handling
  Error cluster
  Checking for errors
  “Raising errors with General Error Handler.vi”

## Slide 83: Homework
From the LabVIEW Help file, read:
  Fundamentals -> Loops and other Structures
  Fundamentals -> Graphs and Charts
From NI’s LabVIEW Core 1 Exercises
  LV1M 3, 4, 5, 6, 9, 15, 17, 18, 21, 22, 23
  Due 2015-04-07

## Slide 84
2015-04-07
84
Phenomenon
Cooling of Tea
Transducer
Thermocouple
Signal Conditioner
Amplifier, Low pass filter
DAQ Hardware
NI CompactDAQ
Computer
Brought to you by IT
Analysis
Curve fitting
Plotting
DAQ
Analog Input
Storing Data
HDF5 Files
Thesis/
Dissertation
Graduate!
Software Basics
Analysis
Curve fitting
Software Basics

## Slide 85: Analysis
LabVIEW has numerous functions for analyzing data
  May not be the best choice for all analysis
  Is your analysis simple, consisting of only a few steps?
  Does your analysis need to be online during your acquisition?
  Do you know exactly what you want to do to analyze your data?
Other choices:
  Diadem
  Igor
  Matlab
  SciPy + NumPy + Python
  It is possible to incorporate analysis functions from Diadem or Matlab into LabVIEW
Some of the palettes with analysis functions
Notes: ChartsAndGraphs.vi

## Slide 86: Simple Analysis
Acquire N measurements, computer average and std. dev.

## Slide 87: Simple Analysis
Apply a low-pass filter
Notes: ChartsAndGraphs.vi

## Slide 88
2015-04-07
88
Phenomenon
Cooling of Tea
Transducer
Thermocouple
Signal Conditioner
Amplifier, Low pass filter
DAQ Hardware
NI CompactDAQ
Computer
Brought to you by IT
Analysis
Curve fitting
Plotting
DAQ
Analog Input
Storing Data
HDF5 Files
Thesis/
Dissertation
Graduate!
Software Basics
Analysis
Curve fitting
Software Basics
Storing Data
HDF5 Files

## Slide 89: Saving Data
What to save?
  Dataset: The raw data (if feasible)
  Intermediate results (standard deviations and other simple processing)
  Attributes:
    Date
    Time
    Purpose of data (comments)
    Acquisition information (instrumentation, settings)
  You can’t save too many details!
    You never know what you’ll wish you had recorded latter
Saving processed results?
  Best to save in separate files
  Use attributes to describe the raw data source and processing methods
Notes: ChartsAndGraphs.vi

## Slide 90: Saving Data: What Format?
File I/O
  Text, CSV
  Raw binary
  Self-describing formats
    TDMS
    NetCDF
    HDF5
    Etc.
Databases
  Use Simple Query Language (SQL) to write, search, etc.
  Data organized in cross-linked tables
  MySQL, postgresql, SQLite, Access, Oracle, etc.
Notes: ChartsAndGraphs.vi

## Slide 91: Data Formats: Preliminaries
I will primarily talk about writing data, not reading it
  Very often, LV is used for acquiring data and saving it
  Decisions are normally made when writing the file. When reading, the decisions are made for you.
In most circumstances, there is no one “right” answer
In most circumstances, there are many wrong answers!
Notes: ChartsAndGraphs.vi

## Slide 92: Text Files
Advantages
Easy to understand
Always work
Portable to any computer
All computers have software that can inspect them
Readable by all processing software
Great for archival data
  100 years from now, Notepad will still exist
Disadvantages
Inefficient
  Disk space
  Processor speed
Difficult to represent higher-order data (>2-D)
Annoying to store attributes
Difficult to show relationships between datasets
Gotchas: Line endings differ from platform to platform (CR, LF, CR+LF)

## Slide 93: Text Files: Delimiters
Data is usually delimited by a character. Common choices are
  Comma
  Tab (my favorite)
  Space
Sometimes data is character column-delimited
  A new field starts at given character column numbers
  Data is padded by spaces or zeros to fill the column
  (See next slide for example)

## Slide 94: Text Files What’s wrong with this file?
Notes: No headers
No attributes
No units

## Slide 95: Text Files Better with column headers
Notes: Column headers with units

## Slide 96: Text Files Header alignment fixed when imported to Excel

## Slide 97: Text Files Even better
Notes: Now with attributes

## Slide 98: Text Files Best practices for writing text files in LabVIEW
Don’t use Write To Spreadsheet File.vi
  No headers, attributes, or good error handling
Do write your own SubVI specific to your data
  Use string function Array to Spreadsheet String liberally
  Write attributes and headers
Develop a file and directory naming convention and stick to it
Watch and learn…

## Slide 99: A Complete CSV Writing VI

## Slide 100: Raw Binary
Advantages
Most efficient (no overhead)
Can store arbitrarily complex data
Complete control over how data is saved
  Useful if application-specific knowledge can save space or time
Disadvantages
Extremely limited software selection
  Only your software can read/write it
Files unintelligible without format documentation
  Don’t lose it!
  Terrible for archival data
Gotcha: Byte order

## Slide 101: Big Endian vs. Little Endian

## Slide 102: What is a self-describing format?
Format that allows arbitrary data to be stored in a binary format
But, format follows an accepted standard
  Contents of the file may be discovered
  Enables data interchange with other software packages
  Enables a generic viewer application
TDMS
CDF

## Slide 103: Self-describing formats
Advantages
More efficient than Text
Many formats can store arbitrarily complex data
Format provides mechanisms for common features
  Higher-order datasets
  Attributes
  Images
Format may allow grouping of datasets
Advantages (cont.)
Not as widely used as text
Less efficient than raw binary
Data customers may not like it
Disadvantages
Data easily inspected
  With format-specific software
Many software packages will be able to read it
  But check first!

## Slide 104: Example: HDF5
Hierarchical Data Format 5
  Data stored in a tree inside the file
  Groups, datasets, attributes
  HDFView application
Native library supports
  C/C++
  FORTRAN
  Java
Also Supported by
  Matlab
    V7.3 .mat files are HDF5
  R
  Igor
  Python (h5py, pytables)
  LabVIEW (Live HDF5)
HDFView
  Viewer application for HDF4 and HDF5

## Slide 105: Simple Live HDF5 Write with Attributes

## Slide 106: Logging Data
Examples shown write all data at the end of the program
For extended experiments, write more frequently
  Don’t risk loosing all the data!
Logging can be done in all formats
Make sure to leave the file open
  Repeatedly opening and closing the file is very time consuming and unnecessary
BEWARE of file buffering
  Data is not written to disk on every software write call
  For efficiency, modern systems wait until a sufficient amount of data is written and then flush it to disk all at once.
  For critical data, force the write by calling the flush call appropriate to your format
  Note that flush is time-consuming

## Slide 107: Logging Data

## Slide 108: Standard Data Streaming
1. Open
(2. Configure)
3. Read/Write
4. Close

## Slide 109: Boolean Behaviors
Boolean buttons can have different behaviors:
  Latch
    Like momentary contact switches
    Once button terminal is read, button returns to original state
  Switch
    Like toggle switches
    Button stays at new state until it is pressed again
  When?
    Pressed: as soon as it’s pressed
    Released: only when the user has released the mouse button
    Until released: activate only while the user has the button pressed
BooleanBehavior.vi

## Slide 110: Design Patterns
So far, most of our VIs have been sequential
  They start
  They read controls and/or acquire data
  They write to indicators and/or files
  They exit
This is not always sufficient
  What if there are multiple processes that you may need?
  What if you need to reconfigure something in the middle?
  What if you want to pause your acquisition?
  What if an error occurs and you’d like to try to recover?
We need a plan
And a while loop
Notes: ChartsAndGraphs.vi

## Slide 111: Design Patterns
Common patterns that solve common problems
  State machine
  Master-slave
  Producer-consumer
  Queued message handler
Patterns may be mixed and matched
  But try not to overdevelop
Templates available for each of the above patterns
  Menu File->New…
  From Template->Frameworks-> Design Patterns
Notes: ChartsAndGraphs.vi

## Slide 112: State Machine
Architecture for responding to events called state changes
State machine can be described by a state chart
Base pattern for any non-sequential program
LV1M36
Suppose a want to have a program that launches one of two programs when the appropriate button is pressed:
Example
Notes: Build LV1M36

## Slide 113: State Machine
LV1M36
Notes: Build LV1M36

## Slide 114: State Machine Maintaining State Info
Complex state machines maintain more information about the state. Called:
  State Data, or
  State Information, or
  The State
Information is used to make state transition decisions
Not all state data may be relevant to all states
Data typically maintained in shift registers in a while loop
Level2a.vi
Notes: Show Level2a

## Slide 115: State Machine Example 2
Requirements
Update clock (date and time) at 1 Hz
Collect data and update graph at 10 Hz
Turn on an indicator if the data value is > 0
User may start and stop processes independently with boolean buttons
Exit VI when stop pressed
Level2a.vi
State data: timers enabled
State data: time expiry
Notes: Show Level2a

## Slide 116: Aside: Making Graphs
Microsoft Visio is the standard tool
Microsoft PowerPoint or other presentation software also works
Vector drawing programs like Illustrator and Inkscape
But, for the truly cheap and lazy I recommend GraphViz (www.graphviz.org)
Source: http://graphs.grevian.org/example

## Slide 117: Event Structure
Responds to events
  FP User events, e.g. “Button pressed”
  DAQ events, e.g. “Data Available”
  Custom events generated by software
  Timeout
Should be called inside a while loop
Gotcha 1: By default, FP is locked while event cases execute
Gotcha 2: Latch-behavior buttons not release until the terminal is read. Therefore, place terminal inside “Value Change” event case.
Timeout (default: never)
Event Selector
Event Info
(growable)
EventDemo Empty.vi
Notes: Build EventDemo Empty.vi

## Slide 118: Level2a w/ Event Structure
Modify Level2a to use event structure

## Slide 119: Aside: Local Variables
Local variable provide additional terminals for controls and indicators.
Terminals may usually be either read or write
  Allows the programmer to read from an indicator
  Allows the programmer to write to a control
Create by right-clicking on
  FP control/indicator
  BD terminal
Change variable direction by right-clicking on local variable
  “Change to read/write”
LocalVariables.vi

## Slide 120: Aside: Local Variables
Local variables should be used sparingly
Avoid using them simply to pass data between loops or other disconnected program parts
  Locals are inefficient
  Locals can be confusing: “Why is this control changing value?!”
  Prefer shift registers, or queues and other synchronization primitives
Usually good uses:
  Programmatic override of control values
  Uh… that’s all I can think of

## Slide 121: Reminder: Continuous Sampling
Acquiring data forever
But how will I graduate?
Specify number of samples to read.
Defaults to “all available.”
See also NI Example: Voltage – Continuous Input.vi
Notes: Modify Finite into Continuous

## Slide 122: State Machines and DAQ
Investigate StateMachineDAQ.vi

## Slide 123: Producer-Consumer Pattern
Built on two concepts:
  Loop parallelism
  Queues
Queues allow messages or data to be passed between independent tasks
  Is a FIFO buffer
  Concept exists in all multi-theaded, multi-process or otherwise multi-tasking languages
  One or more tasks/loops enqueue elements into the queue
  One task dequeues the elements and processes them
  LabVIEW: Programming -> Synchronization -> Queue Operations palette
Notes: Build EventDemo.vi

## Slide 124: Producer-Consumer Pattern
Producer Loop
Data Enqueued
Consumer Loop
Data Dequeued
Queue Created
Queue Reference
Notes: Build a demo from the Producer-Consumer pattern.

## Slide 125: Message Passing Pattern

## Slide 126: Review: Lectures 3 and 4
Analysis
  LabVIEW can do it
  Often helpful to process online to know if results are good
When choosing a data format consider:
  Who’s using it and when?
  Portability
  File size
  Archival needs
Text files
  Good for 1 or 2 dimensional data
  Always write column headers
  Write attributes at the top of the file
Self-describing formats
  Usually the best choice
  Can be both powerful and easy to use
Design patterns
  Solve common problems
  Templates are available in LabVIEW
State Machine
  Most non-sequential programs use it
  States control the execution
  Decisions are made to change the state
  State information is maintained
    Shift registers in LabVIEW